## Slide 1
Air Quality Model Evaluation
Ensuring Reliable and Accurate
Air Quality Forecasts
Sara Basart (sbasart@wmo.int)
Scientific Officer, Science and Innovation Department
Training Course on Seamless Prediction of Air Pollution in Africa, 12-25 September 2024

## Slide 2
UN specialized agency on weather, climate and water.
Supported by 193 Members and headquarters in Geneva (Switzerland).
Coordinates work of > 300,000 national experts from meteorological and hydrological services, academia and private sector.
Co-founder and host agency of IPCC.
World Meteorological Organization (WMO)

## Slide 3
Atmospheric Composition
on the Global context: Wildfires
(Lasslop et al., 2019)
(IPCC, 2021)
Lower emissions that would limit the global temperature increase to <2°C would reduce projected increases of global burned area to 30% to 35% and projected increases of fire frequency to ~20%.

## Slide 4
WMO Technical Departments
Including specific activities on SDS, wildfires and air quality forecasting
GCOS
G3W
WIPPS
EW4All

## Slide 5
Advance and enhance science, services and infrastructure related to atmospheric composition, and support policies for society through applied research aimed at improving the understanding of the roles of aerosols, reactive gases, stratospheric ozone and greenhouse gases and their interactions in the Earth System.
Drivers: Global societal needs
WMO Research - Global Atmosphere Watch (GAW) Research Enabling Atmospheric Composition Services
Notes: The GAW programme is focused on research enabling atmospheric composition services through providing high quality observations and better representing these processes in Earth System Models.

## Slide 6: WMO Research - Science for Services
Sand and Dust Storm SDS-WAS
Vegetation Fire and Smoke Pollution VFSP-WAS
Global Air Quality Forecasting and Information System (GAFIS)
Advance the application of atmospheric composition information in support of policies and conventions, and expand societal services related to air quality, human and ecosystem health, climate change and food production.
Warnings and Forecasting Services
Model intercomparisons
Notes: The GAW programme is focused on research enabling atmospheric composition services through providing high quality observations and better representing these processes in Earth System Models.

## Slide 7
GAW Station Information System (GAWSIS, https://gawsis.meteoswiss.ch/GAWSIS/#/) part of WMO Integrated Global Observation Systems (WIGOS)
Strengthen the atmospheric composition measurement and data infrastructure and contribute to understanding trends and variability and extremes.
- More than 200 parameters
- Intercomparisons
- Measurement guidelines
- World Data Centers
Filling gaps:
LCS and satellites, but also National AQ networks
  Open access with emphasis in QA and QC
Research Infrasctructure for the provision of Services
Notes: SO A with figure 5 observational infrastructure.
Activity SO-A1: Enable a fully traceable, world-scale observing system for atmospheric composition guided by requirements (GCOS, OSCAR).
Activity SO-A2: Strengthen coordination of atmospheric composition measurement and data infrastructure.
Activity SO-A3: Respond to emerging needs and emerging technologies.
Activity SO-A4: Strengthen policies that support the importance of atmospheric composition data.

## Slide 8
Forecasting - Model Intercomparisons:
Sand and Dust Storms
Wildfires
Air Quality
WMO INFRASTRUCTURE - WIPPS
Regional Specialized Meteorological Center with activity specialization
GHG emission information systems – IG3S city projects
Research Infrasctructure for the provision of Services

## Slide 9
WMO Sand and Dust Storms Warning Advisory and Assessment System (SDS-WAS)
https://community.wmo.int/en/activity-areas/gaw/science-for-services/sds-was
International coordination of research for weather and climate
Identification and assessment of SDS impacts
Dissemination and awareness
Promoting the use of current available SDS products
Godzilla, June 2020
Building capacity and facilitate access to the available services

## Slide 10
Modelling and Observations

## Slide 11
Accuracy & Reliability:
  Models need to predict pollutant concentrations with high accuracy.
Regulatory Compliance:
  Ensure models meet national and international air quality standards.
Key Steps in Model Evaluation
Comparison with Observations:
    Validate model output against measured air quality data (points: ground-based, gridded: satellite).
Statistical Performance Metrics:
    Categorical: Definition of categories by intensity
      Contingency tables
    Continuous
      Metrics like Mean Bias (MB), Root Mean Square Error (RMSE), and correlation coefficients.
Why do we evaluate air quality models?
VISUALISE THE RESULTS MATTERS!

## Slide 12
http://dust.aemet.es
@dust_barcelona
Model intercomparisons
1. Promoting best practices and guidelines to be used by the international community
2. Development of probabilistic forecasts
ONLY DUST

## Slide 14
Understanding the observations
Aerosol typing – Example AERONET
(Basart et al., 2012)
Size
Angstrom Exponent
α(440,870 nm)
Mixture
Angstrom Exponent
Curvature
α(440,675nm)–α(675,870nm)
Intensity
AOD 440 nm

## Slide 15
http://dust.aemet.es
@dust_barcelona
Systematic underestimations in summer in Tamanrasset (Algeria)
ONLY DUST

## Slide 16
Understanding the forecast | Spatial resolution
Example of NO2
(Benavides et al., 2021)
CALIOPE AQ forecasting system
Barcelona, Spain, ​9-25 November 2017

## Slide 17
Understanding the forecast | Representativity
(Benavides et al., 2021)
CALIOPE AQ forecasting system​
Barcelona, Spain, ​9-25 November 2017

## Slide 18
https://aeroval.met.no/pages/evaluation/?project=cams2-82

## Slide 19
https://aeroval.met.no/pages/evaluation/?project=cams2-82
Understanding the processes
NO2 is the precussor of O3

## Slide 20
Understanding the observations
Measurement technique, NO2 bias
Courtesy of Dene Bodwalo
There is a known bias associated to the chemilluminescence method used to mesured NO2. When using an internal molybdenum converter, is essentially a fraction of NOx, overestimating NO2.

## Slide 21
Understanding the observations
Measurement limitations
Limit of detection The most impacted sites were “saturated” (i.e. recorded values lower than reals)

## Slide 22
Understanding the observations
Should we take all data?
Courtesy of Dene Bodwalo
Each model evaluation will have sligthly different objectives, and how strict you wish to be in screening observations will depend upon these objectives
On a very simplistic level, deciding whether or not to keep zero measurements can vary between evaluations (i.e. statistics)

## Slide 23
http://dust.aemet.es
@dust_barcelona
Fair comparison
MODIS is on board of a polar satellite.
This means two overpasses per day over the same region.
ONLY DUST

## Slide 24
Understanding the forecast | Regridding and interpolations
Spatial regridding refers to the process of transforming model data from one grid resolution or structure to another.
There are different interpolation methods (nearest neighbor, bilinear interpolation, cubic spline, ...)
  Check artifacts! Ensure that regridding does not introduce unrealistic patterns or distortions in the data.
Tools CDO, EMSF, xEMSf

## Slide 25
Key Messages
Design your evaluation for the purpose
  Continuous vs categorical
  Observations (point vs grid)
  Selection of your plot, graph, map...
Compare oranges with oranges
  Comparison of the same parameter
  Understand the spatial and temporal representativity of the stations or gridded datasets
Understand your model
  Be sure about the scales that you are considering in your configuration and the processes represented
OPEN DATA and OPEN SCIENCE, Clear Skies: Improving Air Quality for a Healthier Tomorrow!

## Slide 26: Thank you.
Sara Basart (sbasart@wmo.int)
https://community.wmo.int/en/activity-areas/gaw
Special thanks to all researchers, providers and users contributing to the WMO initiatives